PART 1     GENERAL

- SUMMARY

  - Section Includes:

    - In-room patient communication boards.

  - Related Sections:

    - Division 1:  Administrative, procedural and temporary work requirements.

- REFERENCES

  - Communication boards and their installation shall comply with applicable provisions of the latest edition of the following standards and with requirements of authorities having jurisdiction:

    - ADAAG – Americans with Disabilities Act Accessibility Guidelines; US Architectural and Transportation Barriers Compliance Board.

    - International Code Council/American National Standards Institute A117.1-Standard on Accessible and Usable Buildings Facilities.

    - National Fire Protection Association 101 Life Safety Code.

- SUBMITTALS

  - Submittals for Review:

    - Approval drawings showing materials, construction detail, lay-out, copy, size and mounting methods.

    - Engineering drawings for each sign type.

    - One sample of each communication board for verification of materials, color, overall quality, and for adherence to drawings and requirements indicated.

- QUALIFICATIONS

  - Manufacturer specializing in manufacturing the products specified in this section with minimum five years experience.  Obtain signs from one source and a single manufacturer.

- WARRANTY

  - Provide manufacturer’s warranty against defects in materials and workmanship for minimum 5 years.

PART 2     PRODUCTS

2.1   MANUFACTURER

- Communication boards shall be View (Additions line) as manufactured by Takeform, 1.800.528.1398, www.takeform.net or Architect approved equal.

B.	Substitutions:  Bidder must obtain prior written approval from the Architect and/or Owner to bid alternates or substitutions to the specification.

2.2   PRODUCT STANDARDS

  - It is the intent of these specifications to establish a visual standard for the Owner including but not limited to signage, free-standing directories, wall organizers, wall sanitizing stations, and communication boards.  All products shall have matching finishes and appearance and constructed utilizing the same fabrication methods to ensure a consistent look throughout.

  - Dimensions and Configuration:

    - Size:  refer to drawings.

    - Configuration:  refer to drawings.

  - Color and Finishes:

    - Face Material:  refer to drawings.

    - Tack board color:  refer to drawings.

    - Insert graphic:  refer to drawings.

    - Metal finish:  refer to drawings.

2.3   COMMUNICATION BOARDS

  - Communication board with dry-erase/magnetic board, tack board, and changeable printed insert.  Refer to drawings for specific configuration.

  - Description:

    - Balance laminated wood composite, powder coated steel marker tray, magnetic steel plate, acrylic non-glare lens and updateable printed graphic.

  - Materials and Construction:

    - Face shall be 0.035” (nominal) standard grade, high pressure surface laminate.

    - The substrate shall be Green 209, a natural fiber wood product.  The sign shall incorporate balanced construction with the core sandwiched between laminates to prevent warping.  An acrylic substrate shall not be acceptable.  Laminate on the face only shall not be acceptable.

    - The laminates (front and back) shall be pressure laminated and precision machined together to a 90-degree angle.  Edges shall be smooth, void of chips, burrs, sharp edges and marks.

    - Dry erase lens shall be 3mm acrylic, surface treated on two sides for abrasion resistance and to prevent marring and scratching.  The acrylic shall also facilitate cleaning and prevent greying and ghosting or five years.

    - Tack board shall be color impregnated, linoleum tackable surface with self-healing properties.  Standard cork board shall not be accepted.

    - The marker tray shall be precision fabricated heavy gauge, powder coated steel.

    - The unit shall utilize a pressure activated adhesive.  The adhesive shall be nonhazardous and shall allow for flexing and deflection of the adhered components due to changes in temperature and moisture without bond failure.

    - Each unit shall be supplied with a single pen holder with magnetic attachment and a quantity of 3 individual magnets.

    - Unit shall cleat mount and shall be provided with mounting template and all hardware for both drywall and masonry surfaces.

  - Printed Inserts:

    - The board shall be equipped with a printed insert to allow changing and updating as required.  The insert shall be polypropylene to withstand routine cleanings.

    - Manufacturer contractor shall provide and install all inserts.

    - Manufacturer shall provide a template containing layout, font, color, artwork and trim lines to allow Owner to produce inserts on laser or ink jet printer.  The template shall be in an Acrobat or Word format (.pdf).

  - Quantities:

Communication Boards:

CC314-A		14”w x 23.38”h x .56”d 		_________________

CC314-B		14”w x 23.38”h x 2”d			_________________

CC314-C		14”w x 23.38”h x 2”d			_________________

CC514-A		22”w x 23.38”h x .56”d		_________________

CC514-B		22”w x 23.38”h x 2”d			_________________

CC514-C		22”w x 23.38”h x 2”d			_________________

CC514-D		22”w x 23.38”h x 2”d			_________________

CC318-A		14”w x 29.88”h x .56”d		_________________

CC318-B		14”w x 29.88”h x 2”d			_________________

CC318-C		14”w x 29.88”h x 2”d			_________________

CC518-A		22”w x 29.88”h x .56”d		_________________

CC518-B		22”w x 29.88”h x 2”d			_________________

CC518-C		22”w x 29.88”h x 2”d			_________________

CC518-D		22”w x 29.88”h x 2”d			_________________

CC322-A		14”w x 36.38”h x .56”d		_________________

CC322-B		14”w x 36.38”h x 2”d			_________________

CC322-C		14”w x 36.38”h x 2”d			_________________

CC522-A		22”w x 36.38”h x .56”d		_________________

CC522-B		22”w x 36.38”h x 2”d			_________________

CC522-C		22”w x 36.38”h x 2”d			_________________

CC522-D		22”w x 36.38”h x 2”d			_________________

CC608-A		29.88”w x 14”h x .56”d		_________________

CC608-B		29.88”w x 14”h x 2”d			_________________

CC608-D		29.88”w x 14”h x 2”d			_________________

CC614-A		29.88”w x 22”h x .56”d		_________________

CC614-B		29.88”w x 22”h x 2”d			_________________

CC614-C		29.88”w x 22”h x 2”d			_________________

CC614-D		29.88”w x 22”h x 2”d			_________________

CC714-A		46.13”w x 22”h x .56”d		_________________

CC714-B		46.13”w x 22”h x 2”d			_________________

CC714-C		46.13”w x 22”h x 2”d			_________________

CC714-D		46.13”w x 22”h x 2”d			_________________

PART 3     EXECUTION

3.1   SITE VISITS

  - Site visits – 3 visits shall be required by the sign contractor:

    - Prior to submission of bid for site assessment and evaluation.

    - Post award for the purposes of meeting with Owners and project manager.

    - Final walk-through and punchlist.

  - Programming – manufacturer shall perform all programming for the purpose of identifying locations.  All programming materials shall be submitted for approval.

3.2   CODE COMPLIANCE

  - It shall be the responsibility of the successful bidder to meet any and all local, state, and federal code requirements in fabricating and installing communication boards.

  - DELIVERY, STORAGE, PROTECTION

- Package to prevent damage or deterioration during shipment, handling, storage and installation.  Products should remain in original packaging until removal is necessary.  Store products in a dry, indoor location.

  - EXAMINATION

- Installer shall examine signs for defects, damage and compliance with specifications.  Installation shall not proceed until unsatisfactory conditions are corrected.

  - INSTALLATION

  - General:  Locate communication boards where indicated using mounting methods in compliance with manufacturer’s written instructions:

    - Manufacturer shall coordinate installation schedules with the Owner and/or Construction Manager.

    - Installation shall be performed by manufacturer’s personnel trained and certified in manufacturer’s methods and procedures.

    - Communication board shall be level, plumb, and at heights indicated with all surfaced free from defects.

    - Upon completion of the work, signage contractor shall remove unused or discarded materials, containers and debris from site.

END OF SECTION