PART 1     GENERAL

- SUMMARY

  - Section Includes:

    - Custom printed self-adhesive wall covering.

  - Related Sections:

    - Division 1:  Administrative, procedural and temporary work requirements.

- REFERENCES

  - Wall covering and its installation shall comply with applicable provisions of the latest edition of the following standards and with requirements of authorities having jurisdiction:

    - National Fire Protection Association 101 Life Safety Code.

    - ASTM – American Society for Testing and Materials E84.

- SUBMITTALS

  - Submittals for Review:

    - Panel schedule in manufacturer's format for verification of graphic image and copy.

    - Approval drawings showing materials, print detail, lay-out, size, graphic and installation method.

    - Elevation drawings.

- QUALIFICATIONS

  - Manufacturer specializing in manufacturing the products specified in this section with minimum 5 years’ experience.  Obtain from one source and a single manufacturer.

- WARRANTY

  - Provide manufacturer’s warranty against defects in materials and workmanship for minimum 5 years.

PART 2     PRODUCTS

2.1   MANUFACTURER

- Wall covering shall be Traffic, Class A Fire Rated, as manufactured by Takeform, 1.800.528.1398, www.takeform.net or Architect approved equal.

B.	Substitutions:  Bidder must obtain prior written approval from the Architect and/or Owner to bid alternates or substitutions to the specification.  Any request for substitutions must be accompanied by a listing of the specific points of deviation.

2.2   STANDARDS

  - Color and Finishes:

    - Colors, patterns and artwork:  see drawings.

    - Graphic Background:  see drawings.

    - Finishes are to meet current federal ADA and all state and local requirements.

2.3   WALL COVERING

  - Wall covering:

    - Wall covering shall be self-adhesive intended for indoor or outdoor use on smooth or textured surfaces.

  - Materials:

    - Wall covering shall be vinyl with a protective overlam included, coated on one side with a removable and repositionable acrylic pressure sensitive adhesive.  Wall covering shall have a thickness of 4 mil.

    - Wall covering shall be printed with UV or latex ink.

    - Wall covering shall have a Type II classification.

    - Wall covering shall have an ASTM E84 Class A/1 flame spread fire rating.

    - Wall covering shall resist mild alkalis, mild acids, salt and water.

    - Wall covering shall be cleanable using mild dish soap and water.

  - Colors, Patterns and Artwork:

    - Refer to drawings.

  - Size:

    - Refer to drawings.

  - Quantities:

    - Refer to drawings.

2.4   INSTALLATION METHOD

- Wall covering shall be allowed to normalize to room conditions for 4-7 days prior to installation and 4-7 days following.  Wall surface shall be flat and smooth or textured, clean and dry.  Wall surface imperfections must be repaired and smoothed.  Walls shall be primed and sealed.

- Wall covering shall have a 1/2” overlap.

PART 3     EXECUTION

3.1   SITE VISITS

  - Site visits – 3 site visits shall be required by the sign contractor:

    - Prior to submission of bid for site assessment and evaluation.

    - Post award for the purposes of meeting with Owners and project manager.

    - Final walk-through and punchlist.

3.2   DELIVERY, STORAGE, PROTECTION

  - Package to prevent damage or deterioration during shipment, handling, storage and installation.  Products should remain in original packaging until removal is necessary.  Store products in a dry, indoor location.

3.3   EXAMINATION

  - Installer shall examine panels for defects, damage and compliance with specifications.  Installation shall not proceed until unsatisfactory conditions are corrected.

3.4   INSTALLATION

  - General:  Installation locations shall be in accordance with specifications.  Locate where indicated using installation methods in compliance with manufacturer's written instructions:

    - The contractor shall coordinate installation schedules with the Owner and/or Construction Manager.

    - Installation shall be performed by manufacturer’s personnel trained and certified in manufacturer’s methods and procedures.

    - The contractor shall submit a CAD generated location plan noting the location of all graphic panels.

    - Panels shall be level, plumb, and at locations indicated with surfaces free from defects.

    - Upon completion of the work, contractor shall remove unused or discarded materials, containers and debris from site.

END OF SECTION