PART 1     GENERAL

- SUMMARY

  - Section Includes:

    - Recognition Displays.

  - Related Sections:

    - Division 1:  Administrative, procedural and temporary work requirements.

- REFERENCES

  - Recognition displays and their installation shall comply with applicable provisions of the latest edition of the following standards and with requirements of authorities having jurisdiction:

    - ADAAG – Americans with Disabilities Act Accessibility Guidelines; US Architectural and Transportation Barriers Compliance Board.

    - International Code Council/American National Standards Institute A117.1-Standard on Accessible and Usable Buildings Facilities.

    - National Fire Protection Association 101 Life Safety Code.

- SUBMITTALS

  - Submittals for Review:

    - Signage schedule in manufacturer's format for verification of text, graphic images, and copy.

    - Approval drawings showing materials, construction detail, lay-out, copy, size and mounting methods.

    - Engineering drawings for each attachment type.

    - Product samples for verification of materials, color, pattern, overall quality, and for adherence to drawings and requirements indicated.

- QUALIFICATIONS

  - Manufacturer specializing in manufacturing the products specified in this section shall have a minimum of five years’ experience.  Display system shall be obtained from one source and a single manufacturer.

- WARRANTY

  - Provide manufacturer’s warranty against defects in materials and workmanship for minimum 5 years.

PART 2     PRODUCTS

2.1   MANUFACTURER

- Recognition displays shall be Applaud as manufactured by Takeform, 1.800.528.1398, www.takeform.net or Architect approved equal.

B.	Substitutions:  Bidder must obtain prior written approval from the Architect and/or Owner to bid alternates or substitutions to the specification.  Any request for substitutions must be accompanied by a listing of the specific points of deviation.

2.2   PRODUCT STANDARDS

  - Engineered and Tested:

    - The display system shall have undergone rigorous testing to ensure longevity and optimal performance.  Testing shall include environmental testing to ensure that materials can withstand changes in temperature and humidity without distortion as well as testing to ensure resistance to chemicals and UV effects.  Further, mechanical testing shall ensure that the tensile and pull-out strength of mounting hardware is adequate to ensure a safe installation.

  - Typography:

    - Type style:  see drawings.  Copy shall be a true, clean, accurate reproduction of typeface(s) specified.  Upper and lower case or all caps shall be as indicated in drawings and message schedule.  Letter spacing to be normal and interline spacing shall be set by manufacturer.

    - Arrows, symbols and logo art:  To be provided in style, sizes, colors and spacing as shown in drawings.

  - Color and Finishes:

    - Colors, patterns and artwork:  see drawings.

    - Message background:  see drawings.

    - Finishes are to meet current federal ADA and all state and local requirements.

2.3   RECOGNITION DISPLAY

  - Display System:

    - The display shall consist of a two-part backer and tile system utilizing a grid that allows tiles to be interchangeable and expandable.

    - Tiles shall be (select, rod mounted, button mounted, magnet mounted, or tape mounted) to backer.

  - Materials:

    - Tile and backer components are available in (select, acrylic, encapsulated acrylic, 6 mm ACM, balanced laminate, solid surface and/or glass).  See drawings.

  - Colors, Patterns, and Artwork:

    - Standard copy colors shall match manufacturer's standard color selection.  See drawings.

    - All images shall have a minimum resolution of 300 dpi and 25% of the enlarge image size.

    - Graphic images.  See drawings.

  - Rod System Attachment:

    - Rod system assemblies shall be comprised of tiles mounted to decorative backers with attachment rods.  See drawings.

    - Rod system assemblies shall utilize 1/4” OD stainless steel rods and rod supports mounted to backer.  Rod supports are 1/16” OD x 1-1/4”h anodized aluminum and mechanically fastened to backers.

    - Tiles shall mount to 1/4” stainless steel rods using 5/8” buttons and standoffs.

    - All material options shall be machined to a 90-degree angle. Edges shall be smooth, void of chips, burrs, sharp edges and marks.

    - All tiles and backers shall be provided with appropriate mounting hardware.  Hardware shall be finished and architectural in appearance.

  - Magnetic System Construction:

    - Magnetic systems shall utilize 1/2” OD x 1/8” thick magnets in backer and tile components.  See drawings.

    - Tile magnets shall be equipped with a silicone pad to preclude movement of the tiles.

    - Backer shall have an integral grid system that allows repositioning of the tiles.  Grid shall enable adding, removing and rearranging of tiles as necessary.

    - All material options shall be machined to a 90-degree angle.  Edges shall be smooth, void of chips, burrs, sharp edges and marks.

    - All tiles and backers shall be provided with appropriate mounting hardware.  Hardware shall be finished and architectural in appearance.

  - Button Mount Attachment:

    - Button systems shall use 3/8” anodized aluminum buttons and 1/4-20 stainless steel set screws to mount tiles to 1/4-20 threaded holes in backers.  See drawings.

    - Tiles shall be mounted (select, flush, 1/4” stood off, or 1/2” stood off) using 1/4”h x 3/8” OD anodized aluminum standoffs.

    - Backer shall have an integral grid system that allows repositioning of the tiles.  Grid shall enable adding, removing and rearranging of tiles as necessary.

    - All material options shall be machined to a 90-degree angle.  Edges shall be smooth, void of chips, burrs, sharp edges and marks.

    - All tiles and backers shall be provided with appropriate mounting hardware. Hardware shall be finished and architectural in appearance.

  - Tape Mount Attachment:

    - Tape system shall utilize tape to mount tiles to backers.  (Note: tiles are permanently attached and not interchangeable).

    - The tape shall be a pressure activated adhesive.  The adhesive shall be nonhazardous and shall allow for flexing and deflection of the adhered components due to changes in temperature and moisture without bond failure.

    - All material options shall be machined to a 90-degree angle.  Edges shall be smooth, void of chips, burrs, sharp edges and marks.

    - All tiles and backers shall be provided with appropriate mounting hardware. Hardware shall be finished and architectural in appearance.

  - Wall Mounting:

    - Recognition systems shall be capable of removing from wall to facilitate painting or cleaning.  No tools shall be required for removal.

    - Recognition systems can be equipped with a locking mechanism to secure panel to wall.  Mechanism shall be hidden from view and shall not require tools to utilize.

PART 3     EXECUTION

3.1   SITE VISITS

  - Site visits – 3 site visits shall be required by the manufacturer:

    - Prior to submission of bid for site assessment and evaluation.

    - Post award for the purposes of meeting with Owners and project manager.

    - Final walk-through and punchlist.

3.2   COMPLIANCE

  - It shall be the responsibility of the manufacturer to meet any and all local, state, and federal code requirements in fabricating and installing recognition display

3.3   DELIVERY, STORAGE, PROTECTION

  - Package to prevent damage or deterioration during shipment, handling, storage and installation.  Products should remain in original packaging until removal is necessary.  Store products in a dry, indoor location.

3.4   EXAMINATION

  - Installer shall examine signs for defects, damage and compliance with specifications.  Installation shall not proceed until unsatisfactory conditions are corrected.

3.5   INSTALLATION

  - Installation, Cleaning and Close-out:

    - Manufacturer shall coordinate installation schedules with the Owner and/or Construction Manager.

    - Installation shall be performed by manufacturer’s personnel trained and certified in manufacturer’s methods and procedures.

    - Display shall be level, plumb, and at heights indicated on drawings.  All surfaces shall be free of defects.  All surfaces shall be wiped down and cleaned following installation.

    - Upon completion of the work, all unused or discarded materials, containers and debris shall be removed from site.

END OF SECTION