PART 1     GENERAL

- SUMMARY

  - Section Includes:

    - Interior ADA compliant signage.

  - Related Sections:

    - Division 1:  Administrative, procedural and temporary work requirements.

- REFERENCES

  - Signs and their installation shall comply with applicable provisions of the latest edition of the following standards and with requirements of authorities having jurisdiction:

    - ADAAG – Americans with Disabilities Act Accessibility Guidelines; US Architectural and Transportation Barriers Compliance Board.

    - International Code Council/American National Standards Institute A117.1-Standard on Accessible and Usable Buildings Facilities.

    - National Fire Protection Association 101 Life Safety Code.

- SUBMITTALS

  - Submittals for Review:

    - Sign finishes, location plan and copy shall be submitted within an interactive web-based database allowing digital review and approval within the context of the floor plans.

    - Approval drawings showing materials, construction detail, lay-out, copy, size and mounting methods.

    - Engineering drawings for each sign type.

    - Sample of two sign types for verification of materials, color, pattern, overall quality, and for adherence to drawings and requirements indicated.

- QUALIFICATIONS

  - Manufacturer specializing in manufacturing the products specified in this section with minimum five years experience.  Obtain signs from one source and a single manufacturer.

- WARRANTY

  - Provide manufacturer’s warranty against defects in materials and workmanship for minimum 5 years.

PART 2     PRODUCTS

2.1   MANUFACTURER

- Signage shall be Lucid as manufactured by Takeform, 1.800.528.1398, www.takeform.net or Architect approved equal.

B.	Substitutions:  Bidder must obtain prior written approval from the Architect and/or Owner to bid alternates or substitutions to the specification.  Any request for substitutions must be accompanied by a listing of the specific points of deviation.

2.2   SIGN STANDARDS

  - It is the intent of these specifications to establish a sign standard for the Owner including but not limited to primary and secondary directories, wall mounted directionals, primary room identification, restrooms, conference rooms, work station ID’s and all code compliant signage.  While the Owner may not obtain all signs and sign types, the signage manufacturer shall design and submit approval drawings for all.

  - Engineered and Tested:

    - The signage system shall have undergone rigorous testing to ensure longevity and optimal performance.  Testing shall include environmental testing to ensure that materials can withstand changes in temperature and humidity without distortion as well as testing to ensure resistance to chemicals and UV effects.  Further, mechanical testing shall ensure that the tensile and pull-out strength of mounting hardware is adequate to ensure a safe installation.

  - Typography:

    - Type style:  see drawings.  Copy shall be a true, clean, accurate reproduction of typeface(s) specified.  Upper and lower case or all caps shall be as indicated in Sign Type drawings and Signage Schedule.  Letter spacing to be normal and interline spacing shall be set by manufacturer.

    - Arrows, symbols and logo art:  To be provided in style, sizes, colors and spacing as shown in drawings.

    - Grade II Braille utilizing perfectly round insertion beads.

  - Evacuation Maps:

    - Evacuation maps shall have unique “you-are-here” orientations as well as two emergency egress paths.  The maps shall show location of fire extinguishers, fire pulls, stairwells, elevators and restrooms.

  - Color and Finishes:

    - Colors, patterns and artwork:  see drawings.

    - Message Background:  see drawings.

    - Finishes shall meet current federal ADA and all state and local requirements.

2.3   SIGNS

  - Signage System:

    - The signage shall consist of an extrusion and tile system utilizing two styles of extrusion, rails and C-channels.  Tiles shall be interchangeable and replaceable within the extrusions.

    - All signs shall have a matching appearance and be constructed utilizing the same manufacturing processes to ensure a consistent look throughout.

  - Materials:

    - Tile components shall be available in (select, non-glare acrylic, clear acrylic, painted acrylic, decorative acrylic, balance laminated high impact polystyrene, 6mm ACM, .080” second surface printed non-glare acrylic face with .125” white acrylic backer, solid surface and encapsulated acrylic).  See drawings.

    - C-channel tile components shall be available in (select, non-glare acrylic, clear acrylic, painted acrylic, decorative acrylic, balance laminated high impact polystyrene, 6mm ACM, .25” non-glare face with .030” first surface printed white applique applied to back, solid surface and encapsulated acrylic).  See drawings.

    - Decorative backers shall be (select, balance laminated high impact polystyrene, 6mm ACM, and .080” second surface printed non-glare acrylic face with .25” white polycarbonate backer).  See drawings.

    - Extrusions shall be 6063-T6 tempered aluminum acid etched and anodized for a smooth, matte, satin finish.  Aluminum shall be 45% remelt billet.

    - The signage shall utilize an acrylic or stainless steel sphere for Grade II Braille.  Braille dots shall be pressure fit into high tolerance holes.  Braille dots shall be domed and protruding a minimum 0.025".

    - For signs installed on glass, a blank backer shall be placed on the opposite side of the glass to cover tape and adhesive.

    - Tactile lettering shall be precision machined, raised 1/32", and matte PETG subsurface colored for scratch resistance.

  - Colors, Patterns, and Artwork:

    - Standard tactile colors shall match manufacturer's ADA standard color selection.  Refer to drawings.

    - Graphic images

        - See drawings.

  - Rail System Construction (Directories, Directionals, Overheads and Suite

Signs):

    - Rail assemblies shall consist of an inner and outer rail.  The inner rail shall mount to the wall while the outer rail is mechanically fastened to the inner rail.  The tiles shall be assembled and secured into the rail assembly using #8-32 stainless steel set screws.

    - Tiles shall be interchangeable enabling moving or replacing as needed.

    - All material options will be machined to a 90-degree angle.  Edges shall be smooth, void of chips, burrs, sharp edges and marks.

    - All signs shall be provided with appropriate mounting hardware.  Hardware shall be finished and architectural in appearance.

  - C-Channel System Construction (Room signs):

    - C-channel system shall consist of an extruded C-channel, tile, and optional insert.  C-channel signs may be used in conjunction with a pictogram.  Pictograms shall be mounted directly to wall.

    - Tiles and inserts shall be replaceable and updateable.  See drawings.

    - Pictograms shall be .125” clear acrylic painted two sides. Signs and pictograms shall be adhered using a nonhazardous pressure activated adhesive.

    - All material options will be machined to a 90-degree angle.  Edges shall be smooth, void of chips, burrs, sharp edges and marks.

    - All signs shall be provided with appropriate mounting hardware.  Hardware shall be finished and architectural in appearance.

PART 3     EXECUTION

3.1   SITE VISITS

  - Site visits – 3 site visits shall be required by the sign manufacturer:

    - Prior to submission of bid for site assessment and evaluation.

    - Post award for the purposes of meeting with Owners and project manager.

    - Final walk-through and punchlist.

  - Programming – sign manufacturer shall perform all wayfinding & programming.  Programming shall include location plan, message schedule, and/or plots, fire/evacuation maps and insert graphics.  All programming materials shall be submitted for approval.

3.2   CODE COMPLIANCE

  - It shall be the responsibility of the successful bidder to meet any and all local, state, and federal code requirements in fabricating and installing signs.

3.3   DELIVERY, STORAGE, PROTECTION

  - Package to prevent damage or deterioration during shipment, handling, storage and installation.  Products shall remain in original packaging until removal is necessary.  Store products in a dry, indoor location.

3.4   EXAMINATION

  - Installer shall examine signs for defects, damage and compliance with specifications.  Installation shall not proceed until unsatisfactory conditions are corrected.

3.5   INSTALLATION

  - General:  Installation locations shall be in accordance with ADA specifications.  Locate signs where indicated using mounting methods in compliance with manufacturer's written instructions:

    - The signage manufacturer shall coordinate installation schedules with the Owner and/or Construction Manager.

    - Installation shall be performed by manufacturer’s personnel trained and certified in manufacturer’s methods and procedures.

    - The signage manufacturer shall submit a CAD generated location plan noting the location of all signage.

    - Installer to conduct a pre-installation survey prior to manufacturing to verify copy and sign location.  Any location discrepancy or message issues shall be submitted to architect for review.

    - Signs shall be level, plumb, and at heights indicated with sign surfaces free from defects.

    - Upon completion of the work, signage contractor shall remove unused or discarded materials, containers and debris from site.

3.6   DIGITAL SIGN MANAGER

  - Manufacturer shall provide a cloud-based, password protected sign management platform enabling the Owner to view and manage their sign assets.  Every sign, sign type, mounting surface, copy, graphic treatment and building location shall be viewable and accessible through the platform.  The online sign management tool shall facilitate sign changes and additions seamlessly updating the system to reflect current conditions.

END OF SECTION