PART 1     GENERAL

- SUMMARY

  - Section Includes:

    - Large format graphic panels.

  - Related Sections:

    - Division 1:  Administrative, procedural and temporary work requirements.

- REFERENCES

  - Graphic panels and their installation shall comply with applicable provisions of the latest edition of the following standards and with requirements of authorities having jurisdiction:

    - ADAAG – Americans with Disabilities Act Accessibility Guidelines; US Architectural and Transportation Barriers Compliance Board.

    - International Code Council/American National Standards Institute A117.1-Standard on Accessible and Usable Buildings Facilities.

    - National Fire Protection Association 101 Life Safety Code.

    - ASTM – American Society for Testing and Materials E84.

- SUBMITTALS

  - Submittals for Review:

    - Panel schedule in manufacturer's format for verification of graphic image and copy.

    - Approval drawings showing materials, construction detail, lay-out, size, graphic and mounting methods.

    - Engineering drawings.

    - ASTM test data for water absorption, temperature, humidity, freeze-thaw, salt spray and flame spread.

- QUALIFICATIONS

  - Manufacturer specializing in manufacturing the products specified in this section with minimum five years experience.  Obtain from one source and a single manufacturer.

- WARRANTY

  - Provide manufacturer’s warranty against defects in materials and workmanship for minimum 5 years.

PART 2     PRODUCTS

2.1   MANUFACTURER

- Panels shall be Moxie, Class A, Fire Rated as manufactured by Takeform, 1.800.528.1398, www.takeform.net or Architect approved equal.

B.	Substitutions:  Bidder must obtain prior written approval from the Architect and/or Owner to bid alternates or substitutions to the specification.  Any request for substitutions must be accompanied by a listing of the specific points of deviation.

2.2   STANDARDS

  - Color and Finishes:

    - Colors, patterns and artwork:  see drawings.

    - Graphic Background:  see drawings.

    - Finishes are to meet current federal ADA and all state and local requirements.

2.3   PANELS

  - Graphic panels:

    - Panels shall be direct printed on ACM.  Panels with a laminated image shall not be acceptable.

  - Materials:

    - Panels shall be fabricated of ACM, 6mm in thickness.  ACM shall be rigid and flat and shall be unaffected by wide fluctuations in temperature and humidity.  Edges shall be smooth without chips, burrs, sharp edge or marks.  The direct print shall be first surface with protective overlay to prevent damage from moisture, UV, scratches and strong cleaning agents.  Colors and general appearance shall be unaffected for 7 years.

    - Panels shall have an ASTM E84, Class A flame spread fire rating.

    - Panels shall comply with ASTM 02247 for water resistance, ASTM D1735 for water fog, ASTM B117 for salt spray and ASTM 02842 for water absorption assuring no degradation of panel, image or overlay.

    - Panels shall comply with ASTM standards for temperature, humidity and freeze-thaw cycles.

    - Panels shall not harbor bacteria and shall withstand use of hospital disinfectants.

  - Colors, Patterns, and Artwork:

    - Vendor shall provide an online library of images including patterns, graphics and photography.  The library shall be organized by idea or theme to facilitate the selection of images appropriate for the project.

    - All images shall have a minimum resolution of 300 dpi and 25% of the enlarged image size.

    - Graphic image(s):

              - See drawings.

  - Panel Size:

    - See drawings.

  - Single or Double-sided:

    - See drawings.

  - Quantities:

    - See drawings.

2.4   INSTALLATION

- All panels shall be provided with appropriate mounting hardware.  See drawings for installation method and hardware type.

- If panel mounting hardware is visible, it shall have a natural, silver finish, architectural in appearance and suitable for the mounting surface.

- Panels shall be capable of removing from wall to facilitate painting or cleaning.  No tools shall be required for removal.

- Panels shall be equipped with a locking mechanism to secure panel to wall.  Mechanism shall be hidden from view and shall not require tools to utilize.

PART 3     EXECUTION

3.1   SITE VISITS

  - Site visits – 3 site visits shall be required by the sign contractor:

    - Prior to submission of bid for site assessment and evaluation.

    - Post award for the purposes of meeting with Owners and project manager.

    - Final walk-through and punchlist.

3.2   CODE COMPLIANCE

  - It shall be the responsibility of the successful bidder to meet any and all local, state, and federal code requirements in fabricating and installing panels.

3.3   DELIVERY, STORAGE, PROTECTION

  - Package to prevent damage or deterioration during shipment, handling, storage and installation.  Products should remain in original packaging until removal is necessary.  Store products flat in a dry, indoor location.

3.4   EXAMINATION

  - Installer shall examine panels for defects, damage and compliance with specifications.  Installation shall not proceed until unsatisfactory conditions are corrected.

3.5   INSTALLATION

  - General:  Installation locations shall be in accordance with specifications.  Locate where indicated using mounting methods in compliance with manufacturer's written instructions:

    - The contractor shall coordinate installation schedules with the Owner and/or Construction Manager.

    - Installation shall be performed by manufacturer’s personnel trained and certified in manufacturer’s methods and procedures.

    - The contractor shall submit a CAD generated location plan noting the location of all graphic panels.

    - Panels shall be level, plumb, and at locations indicated with panel surfaces free from defects.

    - Upon completion of the work, contractor shall remove unused or discarded materials, containers and debris from site.

END OF SECTION