PART 1     GENERAL

- SUMMARY

  - Section Includes:

    - Silicone edge graphic panels (illuminated).

  - Related Sections:

    - Division 1:  Administrative, procedural and temporary work requirements.

- REFERENCES

  - Graphic panels and their installation shall comply with applicable provisions of the latest edition of the following standards and with requirements of authorities having jurisdiction:

    - ADAAG – Americans with Disabilities Act Accessibility Guidelines; US Architectural and Transportation Barriers Compliance Board.

    - International Code Council/American National Standards Institute A117.1-Standard on Accessible and Usable Buildings Facilities.

    - National Fire Protection Association 101 Life Safety Code.

    - ASTM – American Society for Testing and Materials E84.

- SUBMITTALS

  - Submittals for Review:

    - Panel schedule in manufacturer's format for verification of graphic image and copy.

    - Approval drawings showing materials, construction detail, lay-out, size, graphic and mounting methods.

    - Engineering drawings.

- QUALIFICATIONS

  - Manufacturer specializing in manufacturing the products specified in this section with minimum five years experience.  Obtain from one source and a single manufacturer.

- WARRANTY

  - Provide manufacturer’s warranty against defects in materials and workmanship for minimum 5 years.

PART 2     PRODUCTS

2.1   MANUFACTURER

- Graphic panels shall be Exude, Class A, Fire Rated as manufactured by Takeform, 1.800.528.1398, www.takeform.net or Architect approved equal.

B.	Substitutions:  Bidder must obtain prior written approval from the Architect and/or Owner to bid alternates or substitutions to the specification.  Any request for substitutions must be accompanied by a listing of the specific points of deviation.

2.2   STANDARDS

  - Color and Finishes:

    - Colors, patterns and artwork:  see drawings.

    - Graphic Background:  see drawings.

2.3   GRAPHIC PANELS

  - Graphic panels:

    - Panels shall be single-sided, internally illuminated, with a dye-sublimination print.

  - Materials:

    - Panels shall be dye-sublimination printed on fabric media.  The fabric shall be printed with custom graphic and have a silicone beading sewn along its perimeter.  The fabric shall be stretched across the frame and the beading shall insert into the frame’s groove.  The graphic shall have no visible sew lines.

    - The frame shall be 3.125” in depth.

    - The frame shall be internally illuminated with LED edge lighting.    Lights shall be positioned on the two longest sides.  Each light strip shall have wide beam angles for light efficiency and low heat.

    - Light color temperature shall be 6500°K.

    - The panel assembly shall have a single power cord extending directly from the frame.

    - The panel assembly shall be UL listed.

    - The frame shall be extruded aluminum with a satin silver anodized finish.  Powder coated black and white shall also be available as well as custom finishes.

    - The frame and graphic assembly will be easily changeable without tools or having to remove frame from wall.

    - The frame shall accommodate graphics up to 50 ft wide and 10 ft high.

    - Frame lengths longer than 93” shall be in two sections and shall be supplied with joiner brackets.

    - The frame and graphic assembly shall have an ASTM E84 Class A flame spread rating.

    - The graphic shall not harbor bacteria and shall be cleanable with common spray cleaners.

  - Panel Size:

    - See drawings.

  - Single or Double-sided:

    - See drawings.

  - Quantities:

    - See drawings.

2.4   INSTALLATION

- All panels shall be provided with appropriate mounting hardware.  See drawings for installation method and hardware type.

- Panels shall be capable of removing from wall to facilitate painting or cleaning.

PART 3     EXECUTION

3.1   SITE VISITS

  - Site visits – 3 site visits shall be required by the sign contractor:

    - Prior to submission of bid for site assessment and evaluation.

    - Post award for the purposes of meeting with Owners and project manager.

    - Final walk-through and punchlist.

3.2   CODE COMPLIANCE

  - It shall be the responsibility of the successful bidder to meet any and all local, state, and federal code requirements in fabricating and installing panels.

3.3   DELIVERY, STORAGE, PROTECTION

  - Package to prevent damage or deterioration during shipment, handling, storage and installation.  Products should remain in original packaging until removal is necessary.  Store products flat in a dry, indoor location.

3.4   EXAMINATION

  - Installer shall examine panels for defects, damage and compliance with specifications.  Installation shall not proceed until unsatisfactory conditions are corrected.

3.5   INSTALLATION

  - General:  Installation locations shall be in accordance with specifications.  Locate where indicated using mounting methods in compliance with manufacturer's written instructions:

    - The contractor shall coordinate installation schedules with the Owner and/or Construction Manager.

    - Installation shall be performed by manufacturer’s personnel trained and certified in manufacturer’s methods and procedures.

    - The contractor shall submit a CAD generated location plan noting the location of all graphic panels.

    - Panels shall be level, plumb, and at locations indicated with panel surfaces free from defects.

    - Upon completion of the work, contractor shall remove unused or discarded materials, containers and debris from site.

END OF SECTION